ANNUAL CONDITION INSPECTION CHECKLIST- AIRPLANE

## AIRCRAFT IDENTIFICATION

| Aircraft |
| --- |
| Manuf: | Schmitt Robert F | Model: | KR2-S | S/N: | 847 |
| N-No: | 1852Z | Owner: | Robert F. Schmitt |
| Engine |
| Manuf: | Revmaster | Model: | 2100D | S/N: | 2874 |
| Propeller |
| Manuf: | Ed Sterba | Model: | LH 54x54 Wood | S/N: | NA |
| Times |
| Acft TT: |  | Eng TT: |  | Prop TT: |  |

| INSPECT THE FOLLOWING ITEMS: | S | U | NOTES/SQUAWKS |
| --- | --- | --- | --- |
| Engine |  |  |  |
| Engine cowling removed |  |  |  |
| Engine exterior for oil leaks |  |  |  |
| Clean engine compartment |  |  |  |
| Compression test #1_____ #2_____ #3_____ #4_____ |  |  |  |
| Valve clearances – Check (.006) |  |  |  |
| Oil- drained & refilled |  |  |  |
| Screen and/or filter for metal particles |  |  |  |
| Engine mount/bushings for condition & security |  |  |  |
| Engine mount attach bolts for proper torque |  |  |  |
| Alternator/generator attachment for condition & security |  |  |  |
| Cylinders for cracks, broken fins, or exhaust stains |  |  |  |
| Engine baffles for condition, security, & cracks |  |  |  |
| Cabin heat, carb heat, & vent ducts for condition |  |  |  |
| Induction system for leaks, deteriorated rubber parts, & loose clamps |  |  |  |
| Carburetor for security & clean inlet screen |  |  |  |
| Carburetor heat air box for condition, security, cracks, & proper operation |  |  |  |
| Engine controls for proper condition, security, proper travel, contact with stops |  |  |  |
| Flexible fuel & oil lines for condition, security, and chafing |  |  |  |
| Oil cooler for condition, security, & leaks |  |  |  |
| Engine cowling for condition, security, & cracks |  |  |  |
| Spark plugs for condition, security, deposits, gap |  |  |  |
| Spark plug reinstallation for proper gaskets, anti-seize, & proper torque |  |  |  |
| Ignition harness for condition, security, routing away from exhaust |  |  |  |
| Ignition lead insulators for condition/cracks |  |  |  |
| Ignition system for proper engine timing or evidence of oil seal failure |  |  |  |
| Oil vent lines for condition, security, & obstructions |  |  |  |
| Fuel System |  |  |  |
| Fuel caps for condition, security, sealing, venting, & proper placarding |  |  |  |
| Fuel tanks for condition, security of mounting, leaks, damage |  |  |  |
| Fuel lines for condition, security of mounting, leaks, proper routing, chafing, flexibility of hoses |  |  |  |
| Fuel filters, strainers, & drains for water or debris- clean |  |  |  |
| Fuel valves for condition, security, leakage, operation, proper detents, & proper placards |  |  |  |
| Fuel level indicators for operation & accuracy |  |  |  |
| Entire fuel system for corrosion |  |  |  |
| Fuel system for adequate fuel flow |  |  |  |
| Exhaust System |  |  |  |
| Stacks for leakage, cracks, chafing on any structure, & condition of slip joints, bracing, gaskets, & flexible couplings |  |  |  |
| Exhaust system for condition & security |  |  |  |
| Exhaust pipes/flanges for condition, security, cracks, evidence of leaks |  |  |  |
| Propeller |  |  |  |
| Propeller for nicks & cracks |  |  |  |
| Propeller for proper track |  |  |  |
| Prop bolts for proper torque & safetying |  |  |  |
| Wood propellers for delamination, decay, security of leading edge tipping, charring of mounting flange |  |  |  |
| Spinner and back plate for cracks |  |  |  |
| Propeller hub or crankshaft flange for cracks or damage |  |  |  |
| General Airframe Inspection |  |  |  |
| Wood structures for water collection, mold, decay, cracks, loose fittings, bond line failures, plywood delaminations, end grain checking, & finish failure |  |  |  |
| Fiberglass & composites for damage, finish failure, heat distortion, delamination, security of previously-repaired areas |  |  |  |
| Transparent plastics for cracks & distortions in the pilot’s field of view |  |  |  |
| Welded tube structures for bends, evidence of overstress, cracks, appearance of weld beads, & corrosion |  |  |  |
| Riveted aluminum structures for evidence of overstress, loose/popped rivets, cracks, & corrosion |  |  |  |
| Fuselage |  |  |  |
| Interior trim panels & seats removed |  |  |  |
| Aircraft cleaned |  |  |  |
| All areas for corrosion |  |  |  |
| All areas for trapped water or ice |  |  |  |
| Interior for loose equipment that might foul controls |  |  |  |
| Door/canopy latching mechanism for condition & security |  |  |  |
| Firewall for distortion and cracks |  |  |  |
| Firewall for holes into cabin area (floodlight test) |  |  |  |
| Behind firewall for loose wires & chafing lines |  |  |  |
| Cockpit fresh air vents & heater vents for condition, security, and operation |  |  |  |
| Seats, seat belts, & shoulder harness for condition, security, and attachment |  |  |  |
| Aircraft data plate in place, in good condition, and correct |  |  |  |
| N-numbers in place, in good condition, correct, & legible |  |  |  |
| “Experimental” placard in place & in good condition |  |  |  |
| Wings & Center Section |  |  |  |
| Access covers removed |  |  |  |
| Structure—appropriate to type of construction |  |  |  |
| All areas for corrosion |  |  |  |
| Drain holes for obstructions |  |  |  |
| All areas for trapped water or ice |  |  |  |
| Wing attach points for security & condition |  |  |  |
| Aileron hinges & trim tabs for condition, security, safetying, & lubrication |  |  |  |
| Empennage/Canard |  |  |  |
| Access covers removed |  |  |  |
| Structure—appropriate to type of construction |  |  |  |
| All areas for corrosion |  |  |  |
| Drain holes for obstructions |  |  |  |
| All areas for trapped water or ice |  |  |  |
| Vertical & horizontal stabilizer attach points for security & condition |  |  |  |
| Elevator, rudder, & trim tab hinges for condition, security, looseness, safetying, & lubrication |  |  |  |
| Landing Gear |  |  |  |
| Jack airplane up |  |  |  |
| All areas for proper lubrication |  |  |  |
| All areas for corrosion |  |  |  |
| Attach bolts & fittings for condition, security, & wear |  |  |  |
| Wheels for condition, security, cracks, faulty bearings, condition of bolts, & lubrication |  |  |  |
| Tires for condition, security, cracks, weather checking, wear, clearance to wheel pants, slippage marks, & proper inflation |  |  |  |
| Tail/Nose wheel for condition, security, cracks, proper travel, broken/loose springs/cables, steering action, & lubrication |  |  |  |
| Brakes for condition, security, lining wear, cracks, & loose rivets |  |  |  |
| Hydraulic brakes for fluid level in reservoir, leaks, condition of hoses/tubing, & service loops on all hoses |  |  |  |
| Master cylinders for condition, proper operation, freedom of movement, leakage, & parking brake operation |  |  |  |
| Instrumentation |  |  |  |
| Pitot-static instruments, hoses, lines, & fittings for condition & security |  |  |  |
| Pitot tube & static port for obstructions |  |  |  |
| Pitot-static system for leakage, if maintenance has been done |  |  |  |
| Electrical instruments, connectors, wires, switches, & circuit breakers for condition, security, & proper operation |  |  |  |
| All instruments for proper placards & markings |  |  |  |
| Compass for compass correction card |  |  |  |
| Electrical System |  |  |  |
| Battery for electrolyte level, charge, terminal insulation, & corrosion |  |  |  |
| Battery box for corrosion, vent & drain lines open, & proper support |  |  |  |
| Charging system components for condition, security, signs of overheating, & cracks/wear/proper tension of drive belts |  |  |  |
| Wiring for condition, security, correct size/type, proper routing, chafing, & security of crimp-on terminals |  |  |  |
| Grounding & bonding straps for condition & security |  |  |  |
| Switches, breakers, & fuseholders for condition, security, proper current/voltage ratings, & proper placards |  |  |  |
| Spare fuses available |  |  |  |
| Electrical devices for condition, security, & proper operation |  |  |  |
| Avionics Installation |  |  |  |
| Equipment, cabling, antennas, circuit breakers, & switches for condition & security |  |  |  |
| All avionics for proper placarding |  |  |  |
| ELT for proper mounting, battery area corrosion, current battery dates, operation of crash sensor, and presence of sufficient radiated signal |  |  |  |
| Flight Control Systems |  |  |  |
| All control systems, through their range of travel, for proper rigging, contact with stops, interference, binding, excessive friction, safetying, damage, corrosion, & lubrication |  |  |  |
| Pushrod control systems for adequate thread engagement of rod ends & clevises, presence/torquing of jam nuts, condition/looseness of rod ends, use of AN970 washers on rod ends, free rotational play in spherical rod ends, & damage/bending/loose rivets in pushrods |  |  |  |
| Control cables for condition, wear, corrosion, kinking, interference, & broken strands |  |  |  |
| Pulleys for wear, alignment with cable, freedom of bearing, condition of pulley brackets, & presence of cable guards |  |  |  |
| Fairleads for wear & 3-degree maximum cable direction change |  |  |  |
| Turnbuckles for presence/condition of safety & a maximum of 3 threads showing |  |  |  |
| All controls for proper placards |  |  |  |
| Control surfaces for repairs that might lead to flutter—weight changes aft of the hinge line, too many coats of paint, trim tab looseness |  |  |  |
| Control surface balance weights for security |  |  |  |
| Engine Run & Operational Inspection |  |  |  |
| Visual inspection of the engine/propeller |  |  |  |
| Oil & fuel present |  |  |  |
| Access covers secure |  |  |  |
| No tools or foreign objects in engine compartment |  |  |  |
| Personnel with fire bottle standing by |  |  |  |
| Brake system check |  |  |  |
| Start engine |  |  |  |
| Oil pressure/oil temperature within limits |  |  |  |
| Coolant temperature within limits |  |  |  |
| Ignition check within limits |  |  |  |
| Static RPM within limits |  |  |  |
| All instruments working & showing proper indications |  |  |  |
| Electrical system operating properly |  |  |  |
| Charging system operating properly |  |  |  |
| COM radio check call returned |  |  |  |
| GPS receiver check- satellite acquisition & accurate present position |  |  |  |
| Taxi test- check brakes & steering |  |  |  |
| Idle rpm within limits |  |  |  |
| Ignition switch “hot mag” test OK |  |  |  |
| Mixture idle cutoff shutdown OK |  |  |  |
| Engine cool down & shut down |  |  |  |
| Entire aircraft- check for oil, hydraulic, or fuel leaks |  |  |  |
| Assure no tools or foreign objects left in aircraft |  |  |  |
| Reinstall engine cowling, access covers, interior access panels, etc |  |  |  |
| Completion |  |  |  |
| All airworthiness directives & manufacturer’s safety directives complied with & recorded in aircraft records |  |  | AD 82-20-01 Bendix Magneto confirmed completed |
| Entries present in aircraft records & within limits for ELT battery expiration dates (2 batteries), last pitot-static system certification date, last transponder certification date |  |  |  |
| Registration certificate, airworthiness certificate, & operating limitations in aircraft |  |  |  |
| Current weight & balance & equipment list available and correct |  |  |  |
| Annual condition inspection logbook entry made & signed |  |  |  |

PERFORMED BY:

| Name: |  | Rating/Cert No: |  |
| --- | --- | --- | --- |
| Date: |  |  |  |